| MIFAB, Inc. | July 2008 |
| --- | --- |
| 1321 West 119th Street |  |
| Chicago, IL 60643-5109 |  |
| Toll Free (800) 465-2736 |  |
| Phone (773) 341-3030 | E-Mail mail@mifab.com |
| Fax (773) 341-3049 | Web Site www.mifab.com |

Product Guide Specification

Specifier Notes: This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format. The section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code. Coordinate this section with other specification sections and the drawings. Delete all “Specifier Notes” when editing this section.

SECTION 22410

WATER CLOSET CARRIERS

Specifier Notes: This section covers MIFAB “MC-10D” double horizontal water closet carrier. Consult MIFAB for assistance in editing this section for the specific application.

PART 1	GENERAL

1.1	SECTION INCLUDES

A.	Double horizontal water closet carriers.

1.2	RELATED SECTIONS

Specifier Notes: Edit the following list of related sections as required for the project. List other sections with work directly related to this section.

A.	Section 22100 - Building Services Piping.

B.	Section 22400 - Plumbing Fixtures and Equipment.

1.3	REFERENCES

A.	ASTM A 48 - Standard Specification for Gray Iron Castings.

1.4	SUBMITTALS

A.	Comply with Section 01330 - Submittal Procedures.

B.	Product Data:  Submit manufacturer's product data, including installation instructions.

1.5	DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage:  Store materials in clean, dry area indoors in accordance with manufacturer's instructions.

C.	Handling:  Protect materials from damage during handling and installation.

PART 2	PRODUCTS

2.1	MANUFACTURER

Specifier Notes: Specify MIFAB, Inc. in the US or MIFAB Canada in Canada

A.	[MIFAB, Inc., 1321 West 119th Street, Chicago, IL. 60643-5109  Toll Free (800) 465-2736.]

Web Site www.mifab.com  E-Mail mail@mifab.com.

2.2	MATERIALS

A.	Water Closet Carriers:  MC-10D double horizontal water closet carrier.

1.	Type:  Double, horizontal adjustable, water closet carrier for back-to-back installations of siphon jet or blowout water closets.

2.	Fitting:  Lacquered, ASTM A 48, Class 25 cast iron.

3.	Waste Connection:  4-inch (100-mm) no-hub.

4.	Vent Connection:  2-inch (50-mm) no-hub.

5.	Carrier Faceplate:  Invertible, lacquered, ASTM A 48, Class 25 cast iron faceplate with removable lugs and elongated mounting slots.

6.	Foot Supports:  Invertible, 18-inch (460-mm) high, ductile iron foot supports with continuous adjustment slots.

7.	Coupling:  Adjustable, ABS coupling with integral test cap.

8.	Bowl Gasket:  Neoprene.

9.	Hardware:  Cadmium-plated hardware.  Chrome-plated cap nuts.

Specifier Notes: Specify required water closet carrier options and revise above text as necessary. Specify length of ABS couplings over 12 inches and cast iron couplings over 7 inches, if specified as options. Delete options not required. Consult MIFAB for additional information.

B.	Water Closet Carrier Options:

1.	Finishing/Tiling Frame:  [Siphon jet]  [Blowout].

2.	ABS Coupling:  [Up to 12 inches]  [Over 12 inches].

3.	Cast Iron Coupling:  [Up to 7 inches]  [Over 7 inches].

4.	Coupling with Horn Adaptor:  [ABS]  [Cast iron].

5.	Auxiliary coupling support for coupling lengths over 12 inches.

6.	Penal fixture back outlet adaptation.

7.	Vandal-proof finish trim.

8.	Women's urinal adaptor.

9.	Hanger-type closet adaptor.

10.	Flush valve support.

11.	Carrier completely factory assembled.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive water closet carriers.  Notify Architect of conditions that would adversely affect installation or subsequent use.  Do not proceed with installation until unsatisfactory conditions are corrected.

3.2	INSTALLATION

A.	Install water closet carriers in accordance with manufacturer's instructions at locations indicated on the drawings.

B.	Install water closet carriers plumb and level.

C.	Anchor foot supports securely to floor with 1/2-inch (13-mm) diameter bolts and anchors.

D.	Install carriers using manufacturer's supplied hardware.

3.3	PROTECTION

A.	Protect installed water closet carriers from damage during construction.

END OF SECTION