Installation instructions for MIFAB’s MI-ROC series of grease interceptors:

1) MI-ROC grease traps have four threaded connections (one on each side of the box)

2) The connection highest from the ground is used for the inlet. One of the other three connections are used for the outlet. The other two connections should be plugged with the three plugs provided.

3) The elbow and the tee provided should be connected to the outlet. Two nipples are provided with every interceptor. One nipple is used to connect the elbow to the outlet and the other nipple is used to connect the elbow to the tee. The tee should be plumbed to a vent as well as the drain/waste line.

4) The interior filter basket should be installed to cover the outlet connection.

Maintenance instructions for MIFAB’s MI-ROC series of grease interceptors:

1) Remove the lid of the grease interceptor to access the body.

2) Scoop the accumulated grease out of the interceptor. This process should be done at least once a week to ensure maximum efficiency of the interceptor.