| MIFAB, Inc. | July 2008 |
| --- | --- |
| 1321 West 119th Street |  |
| Chicago, IL 60643-5109 |  |
| Toll Free (800) 465-2736 |  |
| Phone (773) 341-3030 | E-Mail mail@mifab.com |
| Fax (773) 341-3049 | Web Site www.mifab.com |

Product Guide Specification

Specifier Notes: This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format. The section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code. Coordinate this section with other specification sections and the drawings. Delete all “Specifier Notes” when editing this section.

SECTION 22150

FLOOR DRAINS

Specifier Notes: This section covers MIFAB “F1100C-S” square floor drain for membrane floor areas. Consult MIFAB for assistance in editing this section for the specific application.

PART 1	GENERAL

1.1	SECTION INCLUDES

A.	Square floor drains for membrane floor areas.

1.2	RELATED SECTIONS

Specifier Notes: Edit the following list of related sections as required for the project. List other sections with work directly related to this section.

A.	Section 22100 - Building Services Piping.

B.	Section 22400 - Plumbing Fixtures and Equipment.

1.3	REFERENCES

A.	ASME A112.6.3 - Floor and Trench Drains.

B.	ASTM A 48 - Standard Specification for Gray Iron Castings.

1.4	SUBMITTALS

A.	Comply with Section 01330 - Submittal Procedures.

B.	Product Data:  Submit manufacturer's product data, including installation instructions.

1.5	DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage:  Store materials in clean, dry area indoors in accordance with manufacturer's instructions.

C.	Handling:  Protect materials and finish from damage during handling and installation.

PART 2	PRODUCTS

2.1	MANUFACTURER

Specifier Notes: Specify MIFAB, Inc. in the US or MIFAB Canada in Canada

A.	[MIFAB, Inc., 1321 West 119th Street, Chicago, IL. 60643-5109  Toll Free (800) 465-2736.]

Web Site www.mifab.com  E-Mail mail@mifab.com.

2.2	MATERIALS

A.	Floor Drains:  F1100C-S square floor drain for membrane floor areas.

1.	Compliance:  ASME A112.6.3.

2.	Load Rating:  Up to 2,000 pounds.

3.	Body:  A1, 8-inch (200-mm) diameter body.  Lacquered, ASTM A 48, Class 25 cast iron body with anchor flange and weepholes.  4-inch (100-mm) throat.  4-inch (100-mm) NPS machined integral body threads.

4.	Strainer:  Reinforced, square, adjustable, nickel bronze strainer with satin finish.  Vandal-resistant stainless steel screws.

Specifier Notes: Specify strainer size and pipe size.

5.	Strainer Size:  [5 inches by 5 inches (125 mm by 125 mm)]  [6 inches by 6 inches (150 mm by 150 mm)]  [8 inches by 8 inches (200 mm by 200 mm)].

6.	Pipe Size:  [2 inches (50 mm)]  [3 inches (75 mm)]  [4 inches (100 mm)]  [6 inches (150 mm)].

7.	Membrane Clamp:  ASTM A 48, Class 25 cast iron membrane clamp ring with primary and secondary weepholes for waterproofing membrane.

Specifier Notes: Specify required floor drain options and revise above text as necessary. Delete options not required. Consult MIFAB for additional information.

B.	Floor Drain Options:

1.	Type 304 stainless steel strainer with No. 4 satin finish.

2.	3M epoxy finish.

3.	Ductile iron grate (8 inches by 8 inches only).

4.	Sediment bucket.

5.	Vandal proof.

6.	Trap seal primer tapping.

7.	Backwater valve.

8.	Acid-resistant epoxy coating.

9.	All galvanized.

10.	Extension.

11.	Body:  [Bronze]  [Type 304 stainless steel]  [Type 316 stainless steel].

12.	Socket Connection Body:  [PVC]  [ABS].

13.	Closure plug.

14.	Deck clamp.

15.	Sump receiver.

16.	Threaded side outlet.

17.	Client logo.

18.	Clamp ring for low rough-in, minimum 5/8 inch (15 mm).

19.	Funnel:  [4-inch round]  [6-inch round]  [4-inch by 9-inch oval]  [6-inch by 3-inch by 1-inch].

20.	Outlet:  [Push-on]  [Threaded]  [Inside caulk].

21.	Elastomeric flange.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive floor drains.  Notify Architect of conditions that would adversely affect installation or subsequent use.  Do not proceed with installation until unsatisfactory conditions are corrected.

3.2	INSTALLATION

A.	Install floor drains in accordance with manufacturer's instructions at locations indicated on the drawings.

B.	Install floor drains plumb, level, and to correct elevation.

C.	Ensure top of floor drains are flush with top of finished floor.

D.	Align sides of square strainers parallel with adjacent walls and pattern of flooring materials.

E.	Install floor drains using manufacturer's supplied hardware.

3.3	PROTECTION

A.	Protect installed floor drains from damage during construction.

END OF SECTION